## Slide 1: Genetically Encoded Labeling Strategies
Kurt Thorn
Nikon Imaging Center, UCSF

## Slide 2: Naturally occurring fluorescent proteins
Fabio Gismondi / Flickr

## Slide 3: Aequorea victoria

## Slide 4: Protein and chromophore structure

## Slide 6: General fluorescent protein info
Monomer size: ~ 240 a.a.; 27 kDa
Many have been engineered from dimeric or tetrameric proteins and may have residual oligomerization
  For GFP variants, A206K ensures monomer
Require oxygen for maturation
Maturation takes ~15 min to hours

## Slide 7: How to evaluate a fluorescent protein?
Excitation and emission wavelengths
  Compatible with filters / lasers?
  Separable from other FPs / dyes?
Brightness
Maturation rate
  May depend on organism and temperature
pH / environment sensitivity
Oligomerization state
Does it perturb fusion protein function?

## Slide 8: Perturbation of fusion proteins

## Slide 9: Good FP combinations
Blue / Green / Red / near IR
  For 405 / 488 / 561 / 640 lasers
  (like DAPI / Fluorescein / Rhodamine / Cy5)
Cyan/ Yellow / Red / near IR
  Good for CFP/YFP FRET

## Slide 10: Recommended Blue FPs
mTagBFP2: 399 ex / 454 em Brightness 32
  Well-matched to 405nm laser
EBFP2: 383 ex / 448 em Brightness 18

## Slide 11: Recommended Cyan FPs
ECFP derived:
mTurquoise2: 434 ex / 474 em Brightness 28
SCFP3A: 433 ex / 474 em Brightness 17
  Folds better than Cerulean and ECFP
Others:
mTFP1: 462 ex / 492 em Brightness 54
TagCFP: 458 ex / 480 em Brightness 21

## Slide 12: Recommended Green FPs
EGFP derived:
mEmerald: 487 ex / 509 em Brightness 37
Superfolder GFP: 485 ex / 510 em Brightness 54
Clover: 505 ex / 515 em Brightness 84
Others:
mWasabi: 493 ex / 509 em Brightness 56
  mTFP1 derivative

## Slide 13: Recommended Yellow FPs
EYFP derived:
mCitrine: 516 ex / 529 em Brightness 58
SYFP2: 515 ex / 527 em Brightness 69
  Improved Venus

## Slide 14: Recommended Red FPs
DsRed derived:
mCherry: 587 ex / 610 em Brightness 16
mApple: 568 ex / 592 em Brightness 37
Others:
TagRFP-T : 555 ex / 584 em Brightness 33
mRuby(2) : 558 ex / 605 em Brightness 39

## Slide 15: Recommended Far-Red / near-IR FPs (Capable of 640nm excitation)
Intrinsically fluorescent:
TagRFP657: 611 ex / 657 em Brightness 3
  Probably not bright enough for routine use
Biliverdin co-factor:
IFP1.4: 684 ex / 708 em Brightness 6
iRFP: 690 ex / 713 em Brightness 6
  Dimeric

## Slide 16: IFP1.4
Chromophore: biliverdin Ixa
Product of heme breakdown
Membrane permeable
321 aa; 36.5kDa
Typically fluorescent in mammalian cells but adding exogenous biliverdin increases fluorescence ~5-fold

## Slide 17: iLOV and relatives
Plant Light, Oxygen, or Voltage sensing (LOV) domains
Bind flavin mononucleotide (FMN)
~100 amino acids
Does not require oxygen

## Slide 18: Optical Highlighter Proteins
Photoactivatable (Off → On)
  PA-GFP, PAmCherry
  PATagRFP
Photoswitchable (Color change)
  mEos2/3
  PS-CFP
Photoswitchable (Off ↔ On)
  asCP, KFP (tetrameric)
  Dronpa
Activate
green
red
before
after
Dendra2 demo

## Slide 19: Photoactivation
Science 2002 297: 1873-1877
Pre-activation
Post-activation
Generally: Off
On
405 nm

## Slide 20: Recommended Photoactivatable Proteins
PAGFP: 504 ex / 517 em Brightness 14 Contrast 100
PAmCherry: 564 ex / 595 em Brightness 8 Contrast 4000
PAtagRFP: 562 ex / 595 em Brightness 25 Contrast 500

## Slide 21: Photoconversion
Generally: Green
Best monomer is probably mEos2 / mEos3.2; multiple tetrameric proteins available
mEos2 (green): 506 ex / 519 em Brightness 47
mEos2 (red): 573 ex / 584 em Brightness 30 Contrast 2000?
Red
405 nm
McKinney et al. Nature Methods 6, 131–133 (2009)

## Slide 22: Photoswitchable – Dronpa
Ando et al. 2004, Science 306: 1370-1373
Generally: Off
On
405 nm
lex

## Slide 23: mIrisFP – Photoswitchable and Photoconvertible
Eos derivative
Both green and red states are decently bright
Green
Red
Off
Off
488
405
405
532
440
Fuchs et al. Nature Methods 7, 627–630 (2010)

## Slide 24: Fluorescent proteins – pros / cons
Can be easily introduced into live cells
Minimally perturbative
Photoactivatible/photoconvertible versions exist
Avoids fixing / staining
Require genetically tractable system
Folding and maturation can be slow
Some are pH and Cl- sensitive
Some have very complicated photophysics (strange photoactivation / photobleaching behavior)

## Slide 25: FlAsH/ReAsH
Labeling protein with tetra-cysteine motifs:
Newly synthesised connexins (ReAsH:Red) are added to the outer edges of existing gap junctions (FlAsH:Green).
Gaietta et al 2002
Commercially available from Invitrogen as Lumio or TC-FlAsH II / TC-ReAsH II

## Slide 26: Covalent attachment of dyes to genetic tags
HaloTag (Promega)
Modified haloalkane dehalogenase
~31 kDa

## Slide 27: Covalent attachment of dyes to genetic tags
SNAP- and CLIP-tags (NEB)
Modified O6-alkylguanine-DNA alkyltransferase; ~20 kDa

## Slide 28: Advantages of HaloTag / SNAP-Tag fusions over GFP:
Same protein can be labeled with almost anything you want
  Easy to couple ligands to any NHS or malemide compound
  Many dye/biotin ligands commercially available
Label same protein in different colours (avoid recloning)
Label different compartments
  Cell-permeable and impermeable probes available
Pulse chase experiments
  Add two different dyes at different time points

## Slide 29: Dye-binding antibodies
Single chain antibodies (scFv) that bind dye molecules
Dyes are only fluorescent in their bound state
  10,000-fold activation possible
Different scFvs bind different dye families
  Can do multicolor labeling
But multiple color dyes can bind same scFv
14 – 26 kDa
Not yet commercially available

## Slide 30: Dye binding antibodies
Membrane permeable dye
Membrane impermeant dye

## Slide 31: Enzyme catalyzed labeling
Genetic Tags:
ACP / MCP Tag (77aa)
YbbR peptide (11aa) (Christopher Walsh)
ACP/SFP synthase (NEB)

## Slide 32: Uses of enzyme catalyzed labeling
1) Site specific labeling of proteins with short peptides
2) Labelling of cell surface proteins
Artificial dimerised dynein with and without YbbR peptide labelled with SFP synthase and 547-CoA (Vale lab)
250kD
150kD
100kD
75kD
-YbbR +YbbR

## Slide 33: Enzyme catalyzed labeling
Biotin or keto-biotin labeling
Ketone group can be specifically labeled
Not yet commercially available
Biotin and Lipoic Acid Ligase (Alice Ting)

## Slide 34: Further Reading
http://nic.ucsf.edu/dokuwiki/doku.php?id=fluorescent_proteins
Nico Stuurman
Mike Davidson
Acknowledgements