## Slide 1
(Image: T. Wittman, Scripps)
Introduction to
Light Microscopy

## Slide 2
The Light Microscope
Four centuries of history
Vibrant current development
One of the most widely used research tools

## Slide 3
A. Khodjakov et al.

## Slide 4: Major Imaging Functions of the Microscope
Magnify
Resolve features
Generate Contrast
Capture and Display Images

## Slide 5
An Upright Epifluorescence Microscope

## Slide 6: What is light?

## Slide 7: Waves vs. Photons vs. Rays
Quantum wave-particle duality
Rays: photon trajectories
Rays: propagation direction of waves

## Slide 8: Wavelength and frequency
c = λν
λ
= 299792458 m/s in vacuum
Wavelength (nm)
ν = 1014 – 1015 Hz

## Slide 9: Rays are perpendicular to wavefronts

## Slide 10: Light travels more slowly in matter
n = 1
n > 1
n = 1
v = c/n
The speed ratio is the Index of Refraction, n

## Slide 11: Refractive Index Examples
Depends on wavelength and temperature
Vacuum 1
Air 1.0003
Water 1.333
Cytoplasm 1.35–1.38 ?
Glycerol 1.475 (anhydrous)
Immersion oil 1.515
Fused silica 1.46
Optical glasses 1.5–1.9
Diamond 2.417

## Slide 12: Refraction by an Interface
Reflected wave
r
Refractive index n1 = 1
Speed = c
Refractive index n2
Speed = c/n
Incident wave
1
Refracted wave
2
n1 Sin(1) = n2 Sin(2)
 Snell’s law:

/n
r = 1
Mirror law:

## Slide 13: Which Direction?
n1
n2 > n1
Refraction goes
towards the normal
in the higher-index medium

## Slide 14: Lenses work by refraction
Incident light
focus
Focal length f

## Slide 15: Ray Tracing Rules of Thumb (for thin ideal lenses)
f
f
Parallel rays converge
at the focal plane
Rays that cross in the focal plane
end up parallel
Rays through the lens center are unaffected

## Slide 16: Imaging
f
The lens law:
Image
Magnification:
L1
L2
Object
d1
d2

## Slide 17: Dispersion
Refractive index is wavelength dependent

## Slide 18: Dispersion

## Slide 19: Diffraction and interference

## Slide 20: Diffraction

## Slide 21: Diffraction by an aperture
See “Teaching Waves with Google Earth” http://arxiv.org/pdf/1201.0001v1.pdf for more

## Slide 22: Interference

## Slide 23: Constructive interference
Δφ
+
=

## Slide 24: Destructive interference
+
=
Δφ

## Slide 25: Thin film interference
harvard.edu
Δφ

## Slide 26: Light propagation = diffraction + interference

## Slide 27: Light propagation = diffraction + interference
A = Σ Ai sin(2πl/λ)
li
Ai
I = A2

## Slide 28: Double slit interference
d

## Slide 29: Double slit interference
d
θ
Δ = d sinθ ≈ dx/z
z
x
Δ = kλ for constructive interference
Stripe distance = ∙ λ

## Slide 30: Diffraction by a periodic structure (grating)

## Slide 31: Diffraction by a periodic structure (grating)

In phase if:
d Sin() = m 
for some integer m
d
d Sin()


## Slide 32: Light as electromagnetic waves
Maxwell’s equations

## Slide 33: Light as electromagnetic waves
Maxwell’s equations
Electric field
Static electric field generated by charges
Charge density
wikipedia

## Slide 34: Light as electromagnetic waves
Maxwell’s equations
Magnetic field
Magnetic force lines form closed circles.
wikipedia

## Slide 35: Light as electromagnetic waves
Maxwell’s equations
Rate of change
A changing magnetic field generates electric field

## Slide 36: Light as electromagnetic waves
Maxwell’s equations
Electric current
Electric current and changing electric field generate magnetic field

## Slide 37: Light as electromagnetic waves
Maxwell’s equations
Michael Davidson

## Slide 38: Polarization
Michael Davidson
wikipedia

## Slide 39: What about energy?
Classically, the energy of light was just the amplitude of the electric and magnetic fields.
But this led to problems….

## Slide 40: Blackbody emission and the UV catastrophe
Max Planck

## Slide 41: Photoelectric effect
The Encyclopedia of Science
Photons are light particles with
Albert Einstein
hν
hν
hν
hν
hν
hν
hν
hν
Photoelectrons

## Slide 42: Properties of Light
Speed: c in vacuum, in matter
Wavelength:
Frequency:
Energy:

## Slide 43: Wave-particle duality
11 electrons
Double-slit experiment of electrons
Akira Tonomura, PNAS, 2005
200 electrons
6000 electrons
40000 electrons
140000 electrons

## Slide 44: Back to Microscopy

## Slide 45: Imaging
f
The lens law:
Image
Magnification:
L1
L2
Object
d1
d2

## Slide 46: Finite vs. Infinite Conjugate Imaging
Object
f0
f0
f0
Object
f0
>f0
f0
Image
Finite conjugate imaging (older objectives)
Image at infinity
Infinite conjugate imaging (modern objectives).
f1
f1
Magnification:
Image
(uncritical)
 Need a tube lens

## Slide 47: Back focal plane
Object
f0
f0
f0
Back focal plane
Rays that leave the object with the same angle
meet in the objective’s back focal plane

## Slide 48: The Compound Microscope
Sample
Objective
Tube lens
Primary or intermediate
image plane
Eyepiece
Back focal plane (pupil)
Exit pupil
Object plane

## Slide 49: The Compound Microscope
Sample
Objective
Tube lens
Intermediate image plane
Eyepiece
Object plane
Back focal plane (pupil)
Exit pupil
Eye
Final image

## Slide 50: The Compound Microscope
Sample
Objective
Tube lens
Intermediate image plane
Eyepiece
Object plane
Back focal plane (pupil)
Exit pupil
Eye
Final image

## Slide 51: The Compound Microscope
Sample
Objective
Tube lens
Intermediate image plane
Eyepiece
Object plane
Back focal plane (pupil)
Exit pupil
Eye
Final image

## Slide 52: The Compound Microscope
Sample
Objective
Tube lens
Intermediate image plane
Eyepiece
Object plane
Back focal plane (pupil)
Exit pupil
Eye
Final image

## Slide 53: The Compound Microscope
Sample
Objective
Tube lens
Intermediate image plane
Projection Eyepiece
Object plane
Back focal plane (pupil)
Secondary pupil
Camera
Final image

## Slide 54: Eyepieces (Oculars)
Features
Magnification (10x typical)
“High eye point” (exit pupil high
enough to allow eyeglasses)
Diopter adjust (at least one
must have this)
Reticle or fitting for one
Eye cups

## Slide 55: Trans-illumination Microscope
Sample
Objective
Tube lens
Intermediate image plane
Projection Eyepiece
Object plane
Back focal plane (pupil)
Secondary pupil plane
Camera
Final image plane
Imaging
path
Aperture iris
Field iris
(pupil plane)
(image plane)
(pupil plane)
Light source
Illumination
path
Collector
Condenser lens
Field lens
The aperture iris
controls the range of
illumination angles
The field iris
controls the
illuminated
field of view

## Slide 56: Köhler Illumination
Object plane
(pupil plane)
(image plane)
(pupil plane)
Sample
Aperture iris
Field iris
Light source
Critical Illumination
Each light source point produces a parallel beam of light at the sample
Uniform light intensity at the sample even if the light source is “ugly” (e.g. a filament)
The source is imaged onto the sample
Usable only if the light source is perfectly uniform

## Slide 57: Conjugate Planes in A Research Microscope

## Slide 58
Two ways:
“Eyepiece telescope”
“Bertrand lens”
How view the pupil planes?