## Slide 1: Phase contrast and DIC
Gerd A. Guenther
2011 Honorable Mention
Nikon Small World photomicrograhy competition
Image of a freshwater ciliate.
Ryan McGorty, UCSF
2013 March 25

## Slide 2: Enhancing contrast: ex post facto

## Slide 3: Why cells have poor contrast?
Cameras and eyes are sensitive to the intensity of light
Amplitude of light wave is altered if object absorbs some light
Amplitude not altered for transparent objects that absorb little (like cells)

## Slide 4: Properties of light
Intensity difference
Color difference

## Slide 5: Ways to achieve high contrast
Contrast depends on instrument and sample.
Exogenous:
  Staining
  Fluorescent labels
  Scattering labels
    Beads, nanoparticles
Intrinsic:
  Absorption
  Scattering
  Phase shift
For cells and thin tissue samples phase shift is all we have to work with.

## Slide 6: Phase Objects
Phase object introduce phase delay of light depending on:
  Index of refraction
  Thickness
Optical path length (OPL):

## Slide 7
Various regions of the brain
From Xie et al., 2012. Optics Express.
Image of smooth muscle cell
1.361
1.357
1.361
Refractive indices of biological samples
1.359
1.364
1.360
From Delbridge, L.M.D et al. 2005. Cytometry Part A.

## Slide 8
Phase difference between two waves depends on the optical path difference (OPD).
Optical path difference = difference in refractive index × distance

## Slide 9: How to observe phase changes?
Must convert difference in phase to amplitude.
Solution: sum shifted wave with some reference

## Slide 10: Interference
Waves that are in phase add constructively.
Waves that are 180° or λ/2 out of phase add destructively.

## Slide 11: Phase contrast microscopy
Devised phase contrast microscopy in 1930s. Received Nobel Prize 1953.
“…it is common knowledge that in all interference phenomena differences of phase are all-important. Why then had phases never been considered before … in the microscope?”
Phases difficult to see
  Must convert phase differences to intensity differences
Phases difficult to define
  Only relative phase matters
Frits Zernike

## Slide 12: Light path for bright-field microscopy
Condenser
Objective
Image plane
Sample plane
Back focal plane
No Sample
Light source
Uniform illumination at the sample plane
At objective’s back focal plane, light occupies small spot
Uniform intensity at the image plane

## Slide 13: Light path for bright-field microscopy
Condenser
Objective
Image plane
Sample plane
Back focal plane
With Sample
Light source
Objective captures light from sample
Light from point in sample focused to point at the image plane
Light from sample occupies larger area in back focal plane

## Slide 14: Light path for bright-field microscopy
With Sample
Light source
Objective captures light from sample
Light from point in sample focused to point at the image plane
Light from sample occupies larger area in back focal plane
Contrast depends on the intensity difference between here and here

## Slide 15
Contrast depends on the intensity difference between here and here
Light source
The microscope image is the interference effect of a diffraction phenomenon.
-Ernst Abbe
Interference at image plane between
  surround or undiffracted light and
  diffracted light.
Contrast depends on intensity of surround light and intensity of surround + diffracted (= particle) light.
For phase objects: diffracted light is 90° out of phase with surround light

## Slide 16: Superposition of two waves, 90° phase difference
Surround
Diffracted
Particle

## Slide 17: Superposition of two waves, 90° phase difference
Surround
Diffracted
Particle
Surround

## Slide 18: Phase contrast microscopy
The microscope image is the interference effect of a diffraction phenomenon.
-Ernst Abbe
Condenser
Objective
Image plane
Sample plane
Back focal plane
Phase plate
Light source
To achieve larger amplitude difference between surround and particle wave: adjust phase difference between surround and diffracted light.

## Slide 19: Phase contrast microscopy
The microscope image is the interference effect of a diffraction phenomenon.
-Ernst Abbe
Light source
Condenser
Objective
Image plane
Sample plane
Back focal plane
Phase plate
Phase plate shifts phase of surround light but has little effect on diffracted light.

## Slide 20: Phase contrast microscopy
Field at the image plane:
… with equations
Add shift to surround:
Addshift to surround:

## Slide 21: Phase contrast microscopy
… with equations
Introduce phase plate:
(Assuming a phase only sample. Notice
Assuming is small:
And :
And :

## Slide 22
Surround wave 90° out of phase with diffracted wave.
Surround wave in phase with diffracted wave.
Particle wave
Surround wave

## Slide 23
Diffracted wave
Particle wave
Surround wave
Negative
Phase Contrast
Positive
Phase Contrast
Vector’s length gives its amplitude. Vector’s angle gives its phase.
Surround wave is rotated by 90° but diffracted wave is untouched.

## Slide 24: Condenser annulus and phase ring
Annulus allows more of the condenser aperture to be used

## Slide 25: Phase Contrast Plates
Annulus plate
Phase plate
Objective
Condenser

## Slide 26: How to get the best contrast?
In addition to introducing a phase shift, phase plate should attenuate the surround wave. Typically, surround wave is reduced by 75%.
Ratio of diffracted light to surround light

## Slide 27
Phase plate is usually a part of the objective.
Condenser annulus and phase plate must be properly aligned for optimal imaging.
Alignment done by observing the phase plate and annulus together in the back focal plane.

## Slide 28: Negative and Positive Phase Contrast Plates
Negative phase contrast
Surround wave travels through more material and is therefore retarded in phase. Materials with larger OPL appear darker.
Positive phase contrast
Surround wave travels through less material and is therefore advanced in phase. Materials with larger OPL appear brighter.
Absorbing material to reduce amplitude of surround wave

## Slide 29: Phase contrast is best for thin samples
Imperfections of phase contrast technique: halo effects and shade-off
Some of the diffracted light enters phase ring and results in halo effect.
Because of larger diffraction from edges, extended objects have “shade-off” in the interiors.

## Slide 30: Example of phase contrast image
Bright field image of neuron.
Phase contrast image.
Notice the halo effect around the body of the neuron.

## Slide 31: Reducing unwanted effects
“Phase contrast microscopy with full numerical aperture illumination,” C. Maurer et al. Optics Express, 16, 19821 (2008).
Some of the diffracted light passes through the phase ring (meant only for the surround light).
Fix: attenuate the diffracted light entering the ring.

## Slide 32: Summary of Phase Contrast
Image = interference of diffracted and surround light
With annulus, surround and diffracted light are separate in back focal plane
phase shift of surround light gives image that depends on phase of objects
Attenuated surround light generates better contrast

## Slide 33: Differential Interference Contrast
Like phase contrast uses interference to convert phase difference to intensity difference
Interferes pairs of neighboring waves that travel close together through sample

## Slide 34: Differential Interference Contrast
Like phase contrast uses interference to convert phase difference to intensity difference
Interferes pairs of neighboring waves that travel close together through sample

## Slide 35: Differential Interference Contrast
Like phase contrast uses interference to convert phase difference to intensity difference
Interferes pairs of neighboring waves that travel close together through sample

## Slide 36: Differential Interference Contrast
Sensitive to phase gradients
Contrast best along the direction of shear
Objects appear shaded or in pseudo 3D relief
Necessary optics: polarizers and prism beam splitters
Uses full condenser and objective apertures
Image of a red blood cell.
OPD = refractive index difference × thickness

## Slide 37: Polarization
Polarization of light is perpendicular to direction of propagation.
Light can be linearly polarized if field is oriented in a single direction.
Light can be elliptically polarized if the field direction rotates as the wave propagates

## Slide 38: Polarization
Polarization of light is perpendicular to direction of propagation.
Light can be linearly polarized if field is oriented in a single direction.
Light can be elliptically polarized if the field direction rotates as the wave propagates

## Slide 39: Birefringence
Wollaston Prism
Birefringent prism splits light into two orthogonally polarized beams.
The two beams transverse the sample and are recombined by another prism.

## Slide 40: DIC: Illumination path
Polarizer
Prism
Condenser lens
Sample plane
Light source
Perpendicular polarizations are displaced by in the sample plane.
Shear distance typically between 0.1 to 1.5 μm depending on objective.

## Slide 41: DIC: Detection path
Perpendicular polarizations are brought back together.
Unless there exists a phase difference between two polarizations, polarizer blocks light (extinction).
Sample plane
Objective lens
Image plane
Prism
Polarizer

## Slide 42
Polarizers
With polarizers crossed (i.e. perpendicular to each other):
  Light is blocked if no phase difference between two displaced light paths
  With phase difference, light is transmitted to a degree depending on the phase difference

## Slide 43
Polarizers
With polarizers crossed (i.e. perpendicular to each other):
  Light is blocked if no phase difference between two displaced light paths
  With phase difference, light is transmitted to a degree depending on the phase difference

## Slide 44
No phase difference between two sheared polarizations:
recombined beam is linearly polarized.

## Slide 45
With a phase difference between two sheared polarizations:
recombined beam is elliptically polarized.

## Slide 46
Ellipticity of combined beam a function of the optical path difference.

## Slide 47
Contrast of image depends on phase difference of the separated polarizations.
Phase differences occur due to:
  Optical path length difference in sample
  Alignment of the two prisms and/or polarizer to introduce a “bias”.

## Slide 48: Control of bias phase
Contrast controlled through “bias retardation” or “compensation”
With no bias, no background light gets through
Bias is introduced through sliding one of the prisms or, with a de Senarmont compensator, rotating a polarizer

## Slide 49: Mathematical description of DIC
Different polarizations sheared by in the sample plane.
The two paths will experience phase shift from the sample, in the limit of small :

## Slide 50: DIC images
Gliksman et al. 1992. J. Cell Biol. 119: 1271-1276.
5 μm
Centriole complex
Microtubules

## Slide 51: Can imaging be quantitative about phase differences?
But these relations hold only for pure phase objects or where the phase of the object is not large.
Many approaches to quantitative phase microscopy:
  Fast Fourier phase microscopy
  Phase-dispersion microscopy
  Spiral phase contrast microscopy
  Optical coherence microscopy
  Digital holographic microscopy
  Etc.

## Slide 52: Spatial light interference microscopy
Can be built into a phase contrast microscope setup
Controllable phase delay of surround light

## Slide 53: Recap
http://zeiss-campus.magnet.fsu.edu/articles/basics/contrast.html

## Slide 54: Recap
http://zeiss-campus.magnet.fsu.edu/articles/basics/contrast.html

## Slide 55
DIC
Phase contrast
Cheek cell
Kidney tissue
Perisarc of hydrozoan

## Slide 56: When to use phase contrast versus DIC?
 | Phase Contrast | DIC
Imaging thick samples | Poor | Good
Imaging with birefringent materials | Good | Poor
Sensitive to sample orientation | No | Yes
Imaging of large phase shifts | Poor | Good

## Slide 57: Additional Resources
Websites:
  http://www.microscopyu.com/
  http://www.olympusmicro.com/
  http://www.leica-microsystems.com/science-lab/
Labs researching quantitative phase imaging:
  Prof. Colin Sheppard http://www.bioeng.nus.edu.sg/optbioimaging/colin/research.asp
  Prof. Gabriel Popescu http://light.ece.illinois.edu/
  Prof. George Barbastathis http://3doptics.mit.edu/website/home
Books:
  Advanced Light Microscopy by M. Pluta
  Introduction to Optical Microscopy by J. Mertz
  Quantitative Phase Imaging of Cells and Tissues by G. Popescu